## Slide 1: HOSPITAL NETWORK SYSTEM
DATA COMMUNICATION & COMPUTER NETWORKS
Group Members

## Slide 2: Overview
Network Topology
Introduction
Network Design
Departmental Structure
IP Addressing
Security Measures
Network Security

## Slide 3: Introduction
Title: "Melbourne Health Services Network Project"
Establishing an independent and secure network infrastructure across two locations.
Branch Department:
Designed to share the workload with the headquarters
Nurses & Surgery Operations (NSO)
Hospital Labs (HL)
Human Resource (HR)
Marketing (MK)
Finance (FIN)
BR-Guest Waiting Area(GWA)
Head Quarter Department:
Houses critical departments such as
Medical Lead Operation & Consultancy Services (MLOCS)
Medical Emergency and Reporting (MER)
Medical Records Management (MRM)
Information Technology (IT)
Customer Service (CS)
Guest Waiting Area(GWA)

## Slide 4: Network Design
Hierarchy:
  Core routers and switches at HQ and branch.
  Departmental segmentation using VLANs.
  Dedicated server-side setup for essential services.
  Two Core routers connected to dual ISPs for redundancy , scalability and optimized network traffic flow
Showcasing core routers, multilayer switches, and access switches at both locations.
Representation of the network layout

## Slide 5: Departmental Structure
Wireless Networks: Implemented across all departments..
HQ Depart: MLOCS, MER, MRM, IT,CS,GWA (Approx. 60 users each)
Branch Depart: NSO, HL, HR, MK, FIN,BR-GWA (Approx. 30 users each)
VLANs and Subnetting: Efficient IP allocation and network isolation.

## Slide 6: IP Addressing
Headquarters IP Allocation:
  MLOCS: Subnet 192.168.100.0/26 (Approx. 60 users)
  MER: Subnet 192.168.100.64/26 (Approx. 60 users)
  MRM: Subnet 192.168.100.128/26 (Approx. 60 users)
  IT: Subnet 192.168.100.192/26 (Approx. 60 users)
  CS: Subnet 192.168.101.0/27 (Approx. 60 users)
  GWA: Subnet 192.168.101.64/27 (Approx. 60 users)
Branch IP Allocation:
  NSO: Subnet 192.168.101.128/27 (Approx. 30 users)
  HL: Subnet 192.168.101.160/27 (Approx. 30 users)
  HR: Subnet 192.168.101.192/27 (Approx. 30 users)
  MK: Subnet 192.168.101.224/27 (Approx. 30 users)
  FIN: Subnet 192.168.102.0/27 (Approx. 30 users)
  BR GWA: Subnet 192.168.101.32/27 (Approx. 30 users)
  Network enables seamless communication among departments, supports wireless networks for user mobility, and facilitates critical services like DNS, Email, and Web hosting through dedicated servers.
  Utilizes the base network of 192.168.100.0 and 192.168.101.0 for departmental IP allocation.

## Slide 7: Security Measures
Device Configurations
  Routers: OSPF, default static routing.
  Layer 3 switches: VLAN setup, Inter-VLAN Routing.
  Dedicated DHCP server: Dynamic IP allocation.
  Switch security measures: ACLs, Port-Security, SSH.
Implemented Security Measures:
  Access Control Lists (ACLs) for traffic control.
  Port-Security on the server-side switch to restrict unauthorized devices.
  SSH for secure remote access via SSH (Secure Shell) for managing devices.
  Site-to-Site IPsec VPN for encrypted communication.
  NAT Overload (PAT) for efficient use of public IPs

## Slide 8: Testing and Validation
Testing Procedures:
Functional & Performance Testing:
  Assess network equipment functionality and performance.
  Measure speed, bandwidth, and latency for optimal performance.
Network Communication:
Inter-departmental Connectivity:
  Ensure smooth data transfer among departments.
  Validate VLAN and Inter-VLAN Routing efficiency.
Security Validation:
ACL & Port-Security Checks:
  Verify traffic control and restricted access measures.